## Slide 1: ANTENNAS FOR ACADEMIC CUBESATS: VHF thru S-Band, What, How and Why
Albert E. Lyerly and Peter W. Pachowicz
George Mason University
Department of Electrical and Computer Engineering, MS 1G5
4400 University Dr., Fairfax, VA 22030
alyerly@masonlive.gmu.edu ppach@gmu.edu

## Slide 2: Contents
1- Motivation and Overview
2 – UHF Antenna ( Data and Command Uplink)
  Dipole
3 – L-Band Antenna ( Command Uplink)
  Monopole
  J-Pole
4 – S-band Antenna ( Data Downlink )
  Linear Patch
  CP Patch
  Feed Methods
5 – Fractal Patch ( Data Downlink)
6 – Tips / Lessons Learned

## Slide 3: MOTIVATION
Large collection of Antenna fundamental and simulation data exist
Teams that followed only simulation results were frequently disappointed in poor or missed Links.
Antenna Performance is influenced by multiple factors, e.g.,
  Implementation
  CubeSat body
  Environment (temperature, UV)
Therefore, we stress realistic expectations
Antenna Testing performed at the Northrop Grumman anechoic chamber

## Slide 4: OVERVIEW
Work dedicated to teams which want to build and fly their own antennas
Frequency Bands: (VHF), UHF, L-band, and S-band
Antennas Reviewed: (Monopole), Dipole, J-pole, 5x5cm patch, and fractal patch
Antennas: Simulated, built, attached to a satellite mockup, and tested
Practical tips provided
Provided designs and results provide guidance for your own designs
It takes 3-5 iterations to design and build your own antenna

## Slide 5: UHF Band Antennas (435-438 Mhz)
What:
  The wavelength is 690 mm. This is large with respect to a CubeSat
    Wire type antennas work well:
      Dipoles,
      Monopoles, J-poles,
      Helix
  Antenna Band Coverage: Omni Directional
Why:
  Mission Requires Antenna coverage that is Omni-directional.
  Pick Dipole. Gain: 2.2 dBi
    Mature Deployment mechanisms
    Easy to tune.

## Slide 6: UHF Band Antennas (435-438 Mhz)
How: Dipole Tuned for Resonance and Minimum Return Loss
  We implemented the λ/2 Dipole on the corner of Cubesat
  Minimum blockage.
The Dipole Elements
  Spring Steel Nitinol- Assist in self deployment. Nitinol maintains or returns to straight
  geometry.
  Requires Temperature stable 1:1 Balun
  Rough Tune Dipole outside of s/c body .
  Final tune dipole deployed on s/c.
  We experience +12 Mhz Shift. Add dipole length to compensate -12 Mhz.
Model Return Loss vs Free space vs Cubesat Body
* Dipole Detuned + 12 Mhz by CubeSat Body

## Slide 7: UHF Band Antennas (435-438 Mhz)
Lessons Learned:
Larger Wire Thickness Improves Return Loss Bandwidth.
  Wide Bandwidth Preferred to compensate for Space Temperature Extremes.
Plot shows Return Loss vs Wire Diameter.
Dipole Tuned to 435.0 Mhz.
Black Solid line: 0.40 mm dia “Thin Diameter ” wire. – Narrow 10 dB BW ( f2 – f1)
Blue Dashed : 2.15 mm “ Medium Diameter Wire”
Green Solid Line: Dia: 6.1mm “ Thick Diameter ” Wire = Wide 10 dB BW.
f1
f2
** Thicker Dipole Wire Increase Return Loss Bandwidth **
Thin Wire: BW 40 Mhz : 9.2 % BW
Medium Wire BW 48 Mhz : 11.0 % BW
Thick Wire BW: 70 Mhz : 16 % BW

## Slide 8: UHF Band Antennas (435-438 Mhz)
½ U Cubesat with UHF Dipole and Balun
0.141 Semirigid 50 ohm Coax Used for electrical rigidity.
Predicted Measured Antenna Pattern
Antenna Coordinate System: +Z axis normal to Antenna Feed Point.
Free space Pattern: Dashed Line.
1.5 dB Ripple in at +45 from S/C blockage
Θ = 90
Φ = 90
Θ = 0
Φ = 0 deg
Model Dipole Directivity w/wo Cube Body
* Gain Oscillation due to Cube Body Blockage *

## Slide 9: UHF Band Antennas (435-438 Mhz)
Measured Return Loss vs Frequency overlay.
Return Loss Measurement difficult –
Radiating dipole Return Los sensitive to nearby objects.
10-15 ft ladder with Cubesat hanging on dielectric rope to
measure stable Return Loss.
Balun Closeup and dipole connection- Keep connections short.
Measured Return Loss vs Model
Return Loss Measurement Requires > 1m clear zone to reduce external Return Loss influence.

## Slide 10: L-Band J-pole Antenna ( 1260.0 – 1270.0 Mhz)
Why:
Uplink alternative to crowded UHF and VHF bands interferers
Deployed antenna geometry designed to protrude beyond the S/C body over Dipole.
Preferred over the Monopole antenna – S/C body used as counterpoise.
178 mm tall.

## Slide 11: L-Band J-pole Antenna ( 1260.0 – 1270.0 Mhz)
What:
Half wave dipole fed at one end. Similar to Dipole. Gain < 2.2 dBi
Quarter wavelength Matching Network clears S/C body
178 mm total length

## Slide 12: L-Band J-pole Antenna ( 1260.0 – 1270.0 Mhz)
How:
λ/4 Short Circuit stub terminates into high impedance.
Feed requires 1: 1 Balun for Balanced Excitation.
50 ohm point easily found by equation, modeling or
on the bench.

## Slide 13: L-Band J-pole Antenna ( 1260.0 – 1270.0 Mhz)
Parallel Line Transmission Line : Spacing S
Return Loss vs frequency vs Spacing S
  Small Spacing : 1.3 % BW @ 0.63 mm
  Medium Spacing: 1.7% BW @ 1.28 mm
  Large Spacing: 2.0 % BW @ 2.03 mm
* Increase Spacing S increase Return Loss Bandwidth

## Slide 14
Predict Gain L-Band J-pole Antenna ( 1260.0 – 1270.0 Mhz)
Model Gain dBi
X - axis
X –pol, ϕ=0
X –pol, ϕ=90
X –pol, ϕ=0
J-pole pattern and gain similar to the Dipole antenna

## Slide 15: L-Band J-pole Antenna ( 1260.0 – 1270.0 Mhz)
Return Loss vs Frequency resonance shows good match with model
Model vs Measured Return Loss Show Good Agreement
Return Loss < 20 dB for 10 MHz BW.
RL: 10 dB for 40 MHz, good margin for Temperature Compensation.
40 MHz
10 MHz

## Slide 16: L-Band J-pole Antenna ( 1260.0 – 1270.0 Mhz)
Lessons Learned
Transmission Line requires attention- Low loss support structure
  Kapton tape used to hold transmission line parallel wires.
1:1 Balun Required to feed parallel transmission line.
Parameter (mm) | Model (mm) | As-Built (mm) | Δ Diff (Model – As-Built) % | Comment
Wire Diameter | 0.813 | 0.813 | 0.0 | 
Lfeed | 3.10 | 3.175 | 2.4 | 
Sinner spacing | 2.03 | 2.0 | 1.4 | 
L1 (λ/2 Dipole) | 106.43 | 112.9 | 6.0 | 
L2 (λ/4 Transmission Line) | 45.90 | 54.2 | 18.0 | Kapton transmission Line poorly predicted
Kapton thickness | 0.254 | 0.254 | 0.0 | 
J-pole built per Model Dimensions then tuned
By clipping J-pole arms.
Copper Wire easy to make shorting stub.

## Slide 17: S-Band RHCP Patch Antenna ( 2.40 - 2.41 Ghz)
What:
Patch geometry – Workhorse in Cubesat Community
  Gain ~ 5 - 6.5 dBi
  Metal conductor separated by a dielectric over a ground plane.
  Support Linear and Circular Polarized antenna.
Field radiate at patch edge.
Antenna field created at patch edge to ground plane.
Useable Gain BW 2 %
Electric field is 0 V/meter at patch center.

## Slide 18: S-Band RHCP Patch Antenna ( 2.40 - 2.41 Ghz)
What cont:
Stripline or Normal Launch available.
Electric Field profile predicts feed point.
50 ohm match without tuning possible.
Electric field is 0 V/meter at patch center.
Two Launch Styles Presented
Microstrip Feed
Pin Feed
For Flight- DC ground patch to prevent
build-up of electric charge.

## Slide 19
S-Band RHCP Patch Predict Antenna Gain ( 2.405 Ghz)
Gain dBi
LHCP, ϕ=0 to 180deg
RHCP
Good Patch design with Axial Ratio < 2.0 dB require Cross Polarization Differential ( RHCP-LHCP > 20 dB)
Predict Gain
Peak Gain 6 dBi

## Slide 20: S-Band RHCP Patch Antenna ( 2.40 - 2.41 Ghz)
How:
Dielectric range Er = 1 to 3.0
Dielectric > 3.0 results in drop in gain.
Return Loss Bandwidth Increase with Dielectric Thickness Increased.
  t= 0.060 inch. RL -10 dB BW = 1.7 %
  t = 0.090 inch. RL -10 dB BW = 2.3 %
Model Return Loss vs Frequency vs Dielectric Thickness
* Patch Impedance BW Increases
with increasing thickness

## Slide 21: S-Band RHCP Patch Antenna ( 2.40 - 2.41 Ghz)
Patch How cont
Goal: Make patch small on S/C to make room for Solar cells etc.
Increase Dielectric and Increase Thickness reduces Patch Size
Trade-offs
High Dielectric Constant Less Gain
High Dielectric Constant Less Bandwidth
Square/Circular Patch = equivalent peak gain.
High ER
Low ER
Circle and Square patch have similar gain.
High ER = decrease patch area, Lower Peak Gain

## Slide 22: S-Band RHCP Patch Antenna ( 2.40 - 2.41 Ghz
Circular Polarization Launched by Location of Chevron.
Numerical Modeling determines 45° Chevron Length
Chart shows Numerical Approach to Low Peak Axial Ratio.
Goal: Maximize RHCP and LHCP Gain Difference.
Best Chevron length L = 2.13 cm
What we Built - Low RF Loss Rogers 6002 Laminate
L
CP patch by adjustment of chevron.

## Slide 23: Measured RHCP Patch Performance 1st Iteration
Patch Tuned for 2.425 Ghz.
Peak Gain 6 dBi.
Poor Cross Polarization ( LHCP gain 1 dB)
( Unwanted LHCP Gain will Rob Desired RHCP Gain)
Patch Return Loss does Not Provide designed CP
fc
Measured Gain
RHCP vs LHCP
Measured Return Loss

## Slide 24
S-Band Linear Polarized Fractal Patch Antenna ( 2.40 - 2.41 Ghz)
Why Fractal Patch
Reduce patch size to free up solar cell or sensor real estate.
  What
    Compared Linear Rectangle Patch with 1st Order Minkowski Patch
    Gain Penalty with Fractal antenna.

## Slide 25
S-Band Linear Fractal Patch Antenna ( 2.40 - 2.41 Ghz)
Comparison
1st Order Minkowski Patch
Dielectric : FR4
Pk Gain3.9 dBi ( Lower )
-15 dB BW: 35.0 Mhz ( 1.4 % BW)
Patch Area: 110.25 cm^2 ( smaller)
Linear Square Patch
Dielectric : FR4
Pk Gain 4.8 dBi ( Higher)
-15 dB BW: 44.0 Mhz ( 1.8 % BW) ( Higher)
Patch Area: 718 cm^2.
( 15.3 % Larger Area than Fractal)

## Slide 26
Model Linear Polarization Square Patch vs Fractal Antenna Gain Comparison
Gain patterns look similar, however Square patch peak gain 1.0 dB higher than the Minkowski Fractal patch. Substrate larger for Fractal patch.

## Slide 27
Measured Square Patch vs Fractal Antenna Comparison
Measured Return Loss Fractal Disagrees with Predict Return Loss Bandwidth. ( Model material properties not correct).
Square Patch vs Fractal Patch Patterns are equivalent. ( Measured and predict show similarity)
FR4 dielectric is inexpensive but RF lossy. Not recommended for high performance antennas or RF circuits.

## Slide 28: Tips and Lessons Learned
Wire Antennas
1) Nitinol Wire connections to RF copper circuit board – We have been successful with Henkel Brand Silver Epoxy.
    Successful in Small Sat launch with Silver Epoxy bond of the Nitinol Wire.
  2) L-Band J-pole was easy to build with needle nose pliers and silver coated copper wire.
    You will have difficulties in bending the short stub with Nitinol Wire.
    The Short Circuit stub can be replaced with a shunt inductor.
Patch Antennas
  3) Rogers 6002 and 5880 Duroid for space antennas. ( Excellent temperature cold to hot stability).
  These 2 Laminates have flight heritage.
  4) Patch bandwidth is narrow!!!! 2 %.
  Expect 3 to 4 iterations to get the frequency centered.
  Design the patch for maximum Bandwidth. Increased Dielectric thickness increases bandwidth.
  We use 1 to 2 oz rolled copper. Rolled copper has less RF loss than Electro deposited Copper.
  We use nickel flash over copper. May save cost over gold plate.
5) Avoid FR4 for RF circuitry. RF Lossy ! At UHF frequencies, I lost 1 dB peak gain due to the use of FR4 material.

## Slide 29: Tips and Lessons Learned
Circular Polarized Patch Antennas- Measurements in the Antenna Range
6) Cross Polarization response is sharp at the patch bore sight.
  To measure Cross Polarization- antenna alignment in bore sight and antenna tilt are critical to measure bore sight cross polarization.
  Good Return Loss at is not equal to minimum Cross Polarization.
    Tune the CP antenna for minimum polarization.
    Tune for Axial Ratio in the antenna range. Then tune for Return Loss.
7) Bonding Soft Duroid to an Aluminum Carrier Plate warpage due to the CTE mismatch.
    Flight worthy with Flight Heritage Laminates: Rogers Duroid 6002 and Rogers 5880. ( Low CTE!)
Fractal Antenna
Not convinced there is a savings in useable patch area by the use of the Fractal Antenna.
  A decrease in antenna gain and antenna bandwidth may not worth this effort.