## Slide 1: A GaN-based Four-Switch Buck-Boost Converter using Ripple Correlation Control for Maximum Power Point Tracking in Dynamic Deep Space Environments
Small Satellite Conference
August 6, 2020
Authors:
Sadab Mahmud, William Collings, Roshan Kini, Ahmad Javaid, Raghav Khanna
University of Toledo
Ansel Barchowsky, Jessica Loveland, Ahmadreza Amirahmadi, Chris Stell
Jet Propulsion Laboratory, California Institute of Technology
Xavier Zapien
Massachusetts Institute of Technology
Presenter: Sadab Mahmud Graduate Student, University of Toledo

## Slide 2: Index
Introduction
Maximum Power Point Tracking (MPPT)
  Ripple Correlation Control (RCC)
Buck-Boost Converter Prototype
Simulation of the MPPT System in SaberRD
Conclusion and Future Works

## Slide 3: Index
Introduction
Maximum Power Point Tracking (MPPT)
  Ripple Correlation Control (RCC)
Buck-Boost Converter Prototype
Simulation of the MPPT System in SaberRD
Conclusion and Future Works

## Slide 4: Introduction
Solar energy is a major contributor of power in most spacecraft.
Spacecraft has increased power requirements due to complex computational and instrumentational needs.
Must be equipped with highly efficient power converters (DC-DC converters).
Power converters must have high power density for minimal mass and volume requirements.
A Spacecraft Model. 1
1https://www.jpl.nasa.gov/missions/active-cavity-irradiance-monitor-satellite-acrimsat/

## Slide 5: Introduction
There are variations in PV output characteristics curve due to rapid changes in solar insolation and temperature. Thus, maximum power point tracking (MPPT) is necessary.
The maximum power point (MPP) of the PV cell changes rapidly during a geosynchronous earth orbital cycle.
Rapid changes in PV MPP in deep space

## Slide 6: Index
Introduction
Maximum Power Point Tracking (MPPT)
  Ripple Correlation Control (RCC)
Buck-Boost Converter Prototype
Simulation of the MPPT System in SaberRD
Conclusion and Future Works

## Slide 7
To ensure the maximum power output from a PV array, the DC-DC converter must be integrated with an MPPT controller.
PV Array
DC-DC Converter
Load
MPPT Controller
IPV
VPV
Duty Ratio
IL
The MPPT system block diagram.
Maximum Power Point Tracking (MPPT)

## Slide 8: Maximum Power Point Tracking (MPPT)
Characteristics PV array power curve. 3
The Ripple Correlation Control (RCC) is a suitable MPPT method which can accurately track the MPP of the PV array in dynamic solar irradiation conditions.
Maximum Power Point (MPP)
PV output characteristic at different solar irradiance levels. 2
2Y. Adel, R. Abdelhady, A. M. Ibrahim, “Assessment of a proposed hybrid photovoltaic array maximum power point tracking method,” in Water Science, vol. 30, no. 2, pp. 108-119, October 2016.
3https://www.seaward-groupusa.com/userfiles/curve-tracing.php

## Slide 9: Ripple Correlation Control (RCC) 4
Inductor Current and Panel Power In-Phase, to the left of MPP. 4
RCC works by correlating the inherent power and inductor current ripples of the DC-DC converter.
Inductor Current and Panel Power Out-of-Phase, to the right of MPP. 4
4T. Esram, J. W. Kimball, P. T. Krein, P. L. Chapman and P. Midya, "Dynamic maximum power point tracking of photovoltaic arrays using ripple correlation control," in IEEE Transactions on Power Electronics, vol. 21, no. 5, pp. 1282-1291, Sept. 2006.

## Slide 10: Ripple Correlation Control (RCC) 4
Output Characteristics Curve of a PV Panel.
Region 1
Region 2
Maximum Power Point
The maximum power point (MPP) can be reached when IL = IL*.
A control law for RCC can be formed as shown below:
Overall, the RCC control law can be expressed as:
where, d = duty ratio for the switch and k = constant
In-phase
Out-of-phase
4T. Esram, J. W. Kimball, P. T. Krein, P. L. Chapman and P. Midya, "Dynamic maximum power point tracking of photovoltaic arrays using ripple correlation control," in IEEE Transactions on Power Electronics, vol. 21, no. 5, pp. 1282-1291, Sept. 2006.

## Slide 11: Advantages of RCC 4
It requires no artificial perturbations; it uses the inherent ripples of voltage or current, which are present in the switching power converter.
It does not rely on any assumptions or characterizations of the PV array.
It can be implemented by using digital microcontrollers.
RCC is a well-established algorithm which can achieve MPP at a fast-tracking rate in rapidly changing atmospheric conditions and solar irradiance.
4T. Esram, J. W. Kimball, P. T. Krein, P. L. Chapman and P. Midya, "Dynamic maximum power point tracking of photovoltaic arrays using ripple correlation control," in IEEE Transactions on Power Electronics, vol. 21, no. 5, pp. 1282-1291, Sept. 2006.

## Slide 12: Index
Introduction
Maximum Power Point Tracking (MPPT)
  Ripple Correlation Control (RCC)
Buck-Boost Converter Prototype
Simulation of the MPPT System in SaberRD
Conclusion and Future Works

## Slide 13: Buck-Boost Converter Prototype
A 4-switch synchronous buck-boost converter was selected to accommodate the wide fluctuations in array voltage observed throughout the course of a mission.
Commercially available GaN transistors were used.
  These GaN HEMTs are tested by NASA JPL and are radiation hardened.
  Can switch with minimal loss at high frequency in MHz range.

## Slide 14: Buck-Boost Converter Prototype
A high power density could be achieved by operating the converter at high switching frequencies.
This system achieved an improved specific power greater than 1kW/kg and a power density greater than 2W/cm3 relative to existing power converters for space application.
A minimum of 5% peak efficiency improvement was observed at output currents greater than 1A.
Parameter | Design Value
Input Voltage | 20 – 100V
Output Voltage | 22 – 36 V
Processing Power | 100 W
Switching Frequency | 1 MHz
GaN Device | GS66516B

## Slide 15: Index
Introduction
Maximum Power Point Tracking (MPPT)
  Ripple Correlation Control (RCC)
Buck-Boost Converter Prototype
Simulation of the MPPT System in SaberRD
Conclusion and Future Works

## Slide 16: Simulation of the MPPT System in SaberRD
A PV array of 2 by 2 panels in a series/parallel configuration was selected.
The simulation was run for 150ms with a change in solar irradiation from 450W/m2 to 900W/m2 in mid-simulation at 75ms.
Change of Solar Irradiation at 75ms

## Slide 17: Simulation of the MPPT System in SaberRD
The panels reach maximum power of ~100W at ~1.5A for 450W/m2 and ~205W at ~3.2A for 900W/m2.
(Left) PV power vs current. (Right) PV power vs voltage.

## Slide 18: Simulation of the MPPT System in SaberRD
The simulation switching frequency was set at 500 kHz, and a developed GaN GS66516B transistor model, was used.
SaberRD Simulation of RCC-based MPPT Digital Controller.

## Slide 19: Simulation of the MPPT System in SaberRD
State Diagrams Used to Define the RCC Algorithm.
PWM Driving Signal Generation
RCC Algorithm
By using the StateAMS tool in SaberRD, a digital controller w/ RCC for the buck-boost converter was designed.

## Slide 20: Simulation of the MPPT System in SaberRD
Simulation results proving the efficacy of the digital RCC based controller:
Output Waveforms of Digital RCC MPPT Simulation.
100W
205W
3.2A
1.5A

## Slide 21: Simulation of the MPPT System in SaberRD
Correlating the results with the PV characteristic curve:
3.2A, 205W
1.5A, 100W

## Slide 22: Index
Introduction
Maximum Power Point Tracking (MPPT)
  Ripple Correlation Control (RCC)
Buck-Boost Converter Prototype
Simulation of the MPPT System in SaberRD
Conclusion and Future Works

## Slide 23: Conclusion and Future Work
This paper has shown that RCC is an excellent MPPT method to achieve accurate and rapid tracking in dynamic space environments.
By using GaN transistors and high switching frequency, a high power density could be attained which is a crucial factor to meet the design constraints for space applications.
The digital controller design demonstrated here could easily and effectively track the PV array MPP.
For future work, different adaptations and modifications of the MPPT RCC algorithm will be explored.

## Slide 24: References
1https://www.jpl.nasa.gov/missions/active-cavity-irradiance-monitor-satellite-acrimsat/
2Y. Adel, R. Abdelhady, A. M. Ibrahim, “Assessment of a proposed hybrid photovoltaic array maximum power point tracking method,” in Water Science, vol. 30, no. 2, pp. 108-119, October 2016.
3https://www.seaward-groupusa.com/userfiles/curve-tracing.php
4T. Esram, J. W. Kimball, P. T. Krein, P. L. Chapman and P. Midya, "Dynamic maximum power point tracking of photovoltaic arrays using ripple correlation control," in IEEE Transactions on Power Electronics, vol. 21, no. 5, pp. 1282-1291, Sept. 2006.

## Slide 25
THANK YOU!
QUESTIONS?
Email: sadab.mahmud@utoledo.edu