## Slide 1
Advanced optimization algorithms increase mission performance and ROI
Smallsat technology and market state enable this approach:
  Substantial computing power available
  Proliferation  need for autonomy
  “Tech demo” posture replaced by maximization of asset capability and ROI
Example (TRL9): Optimized attitude slew maneuvers generate more remote sensing ROI per orbit
Bryan Rogler, Matt Baumgart, Elvis Silva
August 6, 2024
AUTONOMOUS ONBOARD OPTIMIZATION IN GNC SYSTEMS
Blue Canyon Technologies - Approved for Public Disclosure This document does not contain technology or technical data controlled under either the U.S. International Traffic in Arms Regulations or the U.S. Export Administration Regulations.

## Slide 2
Autonomously calculates and executes optimal attitude maneuver trajectories
TRL9 across multiple missions and customers:
  Exists in core Blue Canyon GN&C flight software
  Accommodates flexible spacecraft
Solved via proprietary black-box nonlinear optimization solver (BCTOPT) running on Blue Canyon flight processor
Example solution:
  180° maneuver about Z axis (no eigenaxis solution exists)
  Trajectory “rides” nontrivial RW operating envelopes
  Nonzero initial/final 3-axis attitude, rate, and acceleration
  Asymmetric SC inertia, spacecraft jerk limit, and more…
OATS: Optimal Attitude Trajectory System
Blue Canyon Technologies - Approved for Public Disclosure This document does not contain technology or technical data controlled under either the U.S. International Traffic in Arms Regulations or the U.S. Export Administration Regulations.

## Slide 3
OATS:
  Integrate CMG dynamics and constraints
    Effect of singularities on optimization process is strongly affected by mathematical formulation
  Added constraint types (e.g. vector keep-out/in)
  Alternative definitions of maneuver “smoothness”
Optimal Orbital Trajectory System (OOTS):
  Autonomous orbital trajectory calculation with onboard propulsion
  Minimizing fuel usage or other objectives
  Configurable to avoid keep out regions in orbital space
FURTHER DIRECTIONS IN WORK
Blue Canyon Technologies - Approved for Public Disclosure This document does not contain technology or technical data controlled under either the U.S. International Traffic in Arms Regulations or the U.S. Export Administration Regulations.