## Slide 1: Hardening Ubuntu for Small Satellite Applications
Matt Palmer - Presenter Ryan Goodner – Co-author Tyler Jordan – Co-author Rich Hunt – Co-author
SAND2024-09691C

## Slide 2: Hardening Ubuntu for Small Satellite Applications
Background
Our payload was put into orbit running Ubuntu Server.
Failure Summary
After booting, due to multiple factors, the root file system partition filled up with cached database files.
Contributing Factors
Read/Write rootfs – Once filled there was almost nothing we could do
Mission apps ran at boot – Complicating the recovery of Flash A
Testing – Failed to find and mitigate this issue before flight
Initramfs
Halting the boot process at the initramfs stage allowed us to clean up and recover.

## Slide 3: Hardening Ubuntu for Small Satellite Applications
OverlayRoot
The Ubuntu package “overlayroot” is used to configure a union mount file system called “overlayfs”.
In our configuration, the rootfs partition is mounted read-only and overlayed with a read-write RAM backed tmpfs file system.
Advantages of Overlayfs
Prevents catastrophic rootfs fill-up
Allows a large read-only rootfs
Simple to setup
Easy to turn on/off
Compatible with swap and separate R/W partitions
Comes packaged with Ubuntu Server
Can be layered or combined with other fault-tolerant file systems like btrfs