## Slide 1
Adaptive Antenna Elevation Masking for Smallsat Constellations
COSMIC-2 Case Study
6 Aug 2024
Billy Gullotta
UCAR/COSMIC
Chris Barsoum (Aerospace), Maggie Sleziak-Sallee (UCAR COSMIC), Ronald Smilek (NOAA/NESDIS/OSPO)

## Slide 2: Antenna Masks & COSMIC-2
Expanded Geographic Coverage
Captured Antenna Tilt Limitations
Original Mask
Inferred Mask
Signal-Inferred Ground Site Masks
Atlas Ghana (COSMIC-2)
NOAA Fairbanks (Sentinel-6)
Mask Raised above obscura
COSMIC-2 Mission
6-smallsat operational Radio Occultation (RO) mission
550-km altitude, 24° inclination
Some products were not meeting latency needs
Identified that lowering contact start elevations could improve latency by adding more contacts
Without the ability to access ground sites quickly to conduct in-situ surveys, how can antenna masks be updated quickly and effectively?
COSMIC-2 Ground Tracks
Antenna Horizon Masks
Define the boundary where antennas will take contacts
Several inputs to determine:
      Line-of-sight obstructions around antenna
        Local RF environment
  Spacecraft transmitter capability
Typically not often updated and conservative
  Especially true for smallsats

## Slide 3: Mission-Specific Architectures
Developed strategy to determine ground site masks using link measurements
Take measurements of signal quality throughout entire visibility
Correlate time of first “good” quality signal with antenna position
Fit a shape of the good azimuth/elevation points
Expanded Geographic Coverage
Captured Antenna Tilt Limitations
Original Mask
Inferred Mask
Signal-Inferred Ground Site Masks
Atlas Ghana (COSMIC-2)
NOAA Fairbanks (Sentinel-6)
Mask Raised above obscura
Real-World Implementation
Performed at a COSMIC-2 ground site and a NOAA site
COSMIC-2 mask change led to expanded coverage and a resultant improvement in data latency
NOAA tests identified limitations in the antenna tilt mechanism during passes for non-polar orbiting spacecraft
COSMIC-2 TEC Latency Before/After Masking Updates
Before
After
Latency (min)
Latency (min)
Both masks were generated through a custom ad-hoc campaign and manually generated → how to scale to larger systems?

## Slide 4: Adding Flexibility and Adaptability
Active Mask Monitoring and Generation
Generate an initial mask using sufficient full visibility passes
Capture and store signal* quality and antenna position data during downlinks
Regularly pull signal quality data and analyze for changes
Re-fit mask to any changes and alert mission and site operators
Antennas
Ground Site Operations
Ground Site
Data Storage
Payload Data
Link Health (per downlink)
Link Health (periodic)
Antenna Masks (periodic)
Mission Operations
Adaptive Mask Generation
Users
Adaptive Antenna Mask Implementation
Benefits
Maximize downlink-able data volumes and downlink opportunities/visibilities
Remote and automated identification of antenna obstructions
Remote detection of issues with signal on both spacecraft and antenna end
Adaptive masking for multiple COSMIC-2 ground sites currently in development
Eb/N0 of spacecraft passes at COSMIC-2 site
RFI identified through mask monitoring
Bad
Good